## Slide 1: SpMV on FPGA fpga101 project Andrea Oggioni

## Slide 2: What is an fpga spmv
Multiplication kernel between a sparse matrix and a vector.
Only store and move the non-zero elements of the matrix in memory (CRS).
Faster than traditional matrix-vector multiplication.
Notes: Sparse = with lots of zeroes
Faster because it skips useless computation (multiplication by zero)
Compressed Row Storage

## Slide 3: How does it work
Target: where is stored in CRS:
  : the vector of non-zero values in the matrix;
  : the vector of the column indexes;
  : the vector of the first column index of each row.

## Slide 4: The algorithm

## Slide 5: Pseudocode
for i = 0 to n – 1 do
y[i] = 0;
for k = r[i] to r[i+1] do
y[i] += a[k] * x[c[i]]
end for
end for

## Slide 6: Implementation
spmv_loop_external:for(VectorSize i = 0; i < MAX_MATRIX_SIDE_SIZE; i++) {
#pragma HLS UNROLL int sum = 0; if(i < numOfRows) {
spmv_loop_internal:for(ValuesSize j = rowPointers[i]; j < rowPointers[i + 1]; j++) {
#pragma HLS PIPELINE II=1 int matrix_value = values[j];
ColumnIndex column_index = columnIndexes[j]; int vector_value = vector[column_index];
int temp = matrix_value * vector_value;
sum += temp;
} }
output[i] = sum;
}
Notes: Unroll external loop into MAX_MATRIX_SIDE parallel units(loop count known at compile time) and activate each unit only if required
Single write per unit on the output
Pipelined with initiation interval = 1

## Slide 7: testbench
Testbench on text file.
Python testcase generator.
Load input
Load target
Call top function
Compare results

## Slide 8: It’s bitstream time
Import IP
Block design
Synthesis
Implementation
Bitstream
Upload files to PYNQ

## Slide 9: Block design
Notes: The kernel parameters are sent over axilite
The kernel loads the data in the vectors from memory through high performance port

## Slide 10: Using the kernel
Allocate buffers
Fill buffers
Write parameters
Start kernel
Wait for termination
Read result
Load overlay

## Slide 11: thanks
Code, slides and report on GitHub
Notes: Listening and for the course and everything